## Slide 1
Presented by:
Wednesday Smith
Public Works
Cross-Connection Control
Backflow Prevention Program
www.kirklandwa.gov/backflow-prevention
Water Use Surveying
Just Do It!

## Slide 2: Just Do It! Art Williams
“Almost everybody in America almost does enough to win. They almost get there. They almost are over the hump. They almost have it going. They almost, in everything they do, almost is a way of life to almost everybody in America. But the winners do it.
What do they do? They do whatever it takes to get the job done. They do it, and do it, and do it, and do it, and do it, until the job gets done. We need leaders in America who can do it.
Art Williams 1-2:37

## Slide 3: ABOUT ME
Durango CO – 2014
Redmond WA – 2016
City of Kirkland – 2020
Current Certifications:
WA DOH
Water Distribution Manager 2 (WDM2)
Backflow Assembly Tester (BAT)
Backflow Assembly Specialty Plumber License (PL30)
IAPMO ASSE INTERNATIONAL
Backflow Prevention Program Administrator
Cross-Connection Control Surveyor
Backflow Prevention Assembly Tester
(International Association of Plumbing and Mechanical Officials & American Society of Sanitary Engineering)
Cross Connection Control Specialist (CCS)

## Slide 4: WHAT IS A CROSS CONNECTION?
A cross connection is a physical connection between a potable (drinkable) water supply and a source of contamination or pollution.
This connection can be created when plumbing is installed, when using certain appliances, or even simply by attaching a hose to a faucet.
Cross connections are not easy to discover but can pose a serious health hazard and threat to water quality.

## Slide 5: Duties of a CCS WAC 246-292-033
A CCS designated by a purveyor as required in WAC 246-292-050(4) shall develop, implement, and
maintain a cross-connection control program that meets the requirements in WAC 246-290-490.
(2) A CCS shall perform the following duties:
  Assess the degree of hazard posed by the consumer's water system to the public water system,
  as required in WAC 246-290-490 (4)(a)(i);
  (b) Determine the appropriate method of backflow protection to prevent contamination of the
  public water system by the consumer's water system, as required in WAC 246-290-490 (4)(a)(ii);
  (c) Inspect backflow preventer installations to verify that the protection provided is appropriate for
the assessed degree of hazard, as required in WAC 246-290-490 (7)(a)(i);
(d) Investigate and respond to backflow incidents known to have contaminated or suspected of
contaminating the public water system, as required in WAC 246-290-490 (3)(h);
(e) Develop and maintain the purveyor's cross-connection control records, as required in
WAC 246-290-490 (3), (4), and (8);
(f) Complete and sign the purveyor's cross-connection control related reports and make the
reports available to the department upon request, as required in WAC 246-290-490(8) including:
  (i) The cross-connection control annual summary reports; and
  (ii) Backflow incident reports after an incident has occurred that contaminated the public water system;
(g) Take corrective action as required in WAC 246-290-490 (2)(h) when a consumer fails to comply with the purveyor’s
cross-connection control requirements regarding the installation, inspection, field testing, maintenance, or repair
of a backflow preventer that protects the public water system; and
(4) As allowed in WAC 246-290-490 (7)(a)(ii), a CCS's duties may include inspecting:
(b) Backflow prevention assemblies to determine if they are installed correctly and approved by the department.

## Slide 6: What kind of hazards are there?
High Health Hazards
  Any substance that if introduced to the public water system could cause serious illness, death or could spread diseases.
Low Health Hazards
  Any substance that if introduced to the public water supply would not be a health hazard but would constitute a nuisance or be aesthetically objectionable.

## Slide 7: What do we do to protect our drinking water?
Assess the degree of hazard posed by the consumer’s water system. Table 12 in the Washington Administrative Codes (WAC) helps determine the appropriate method of backflow prevention.
Degree of Hazard | Application Condition | Appropriate Approved Backflow Preventer
High health cross-connection hazard | Backsiphonage or backpressure backflow | Air Gap, RPBA**, or RPDA**
Low cross-connection hazard | Backsiphonage or backpressure backflow | Air Gap, RPBA**, RPDA**, DCVA**, or DCDA**
The purveyor shall ensure that an approved air gap, RPBA, or RPDA is installed for premises isolation for service connections to premises posing a high health cross-connection hazard including, but not limited to, those premises listed in Table 13 (next page).
WAC 246-290-490 Cross Connection Control – Table 12 (Previously Table 8)
Appropriate Methods of Backflow Protection for Premises Isolation
**RPBA – Reduced Pressure Backflow Assembly, RPDA – Reduced Pressure Detector Assembly, DCVA – Double Check Valve Assembly, DCDA – Double Check Detector Assembly

## Slide 8: WAC 246-290-490 Cross Connection Control Severe and High Health Cross-Connection Hazard Premises Requiring Premise Isolation by Air Gap (AG) or Reduced Pressure Backflow Assembly (RPBA)
Agricultural (farms and dairies)
Beverage bottling plants
Car washes
Chemical plants
Commercial laundries and dry cleaners
Premises where both reclaimed water and potable water are provided
Film processing facilities
Food processing plants
Hospitals, medical centers, nursing homes, veterinary, medical and dental clinics, and blood plasma centers
Premises with separate irrigation systems using the purveyor's water supply and with chemical addition+
Laboratories
Metal plating industries
Mortuaries
Petroleum processing or storage plants
Piers and docks
Radioactive material processing plants or nuclear reactors*
Survey access denied or restricted
Wastewater lift stations and pumping stations
Wastewater treatment plants*
Premises with an unapproved auxiliary water supply interconnected with the potable water supply
TABLE 13 (Previously Table 9)
Air Gap
RP Models
Min.
1”

## Slide 9: Backflow Assemblies Clearance and Accessibility Requirements
Backflow prevention assemblies are critical components that protect the potable water systems from pollution or contamination sources. It is important to remember a backflow preventer is a mechanical device which requires testing and at some point, in time will require replacement or repair.
Uniform Plumbing Code (UPC)
603.4.3 Access and Clearance:
Access and clearance shall be provided for the required testing, maintenance, and repair.

## Slide 10
WA DOH
(b) The purveyor shall ensure that approved backflow preventers are installed in a manner that:
(i) Facilitates their proper operation, maintenance, inspection, in-line testing, and repair using standard installation procedures acceptable to the department such as those in the USC Manual or PNWS-AWWA Manual;

## Slide 12
PNW-AWWA

## Slide 13
All newer homes have hose bibs that have an internal atmospheric vacuum breaker (AVB) built in. But in older homes they do not have any protection. A simple hose bib vacuum breaker adapter is an easy solution for those who want to use a hose.
AVB’s are designed with a disk that seals against the diaphragm which closes the check allowing the operating vent ports open.
Facts you should know about an AVB:
The AVB is a non-testable device and cannot be under continuous pressure, as the poppet would likely stick and the AVB would no longer function properly. Shutoff or control valves should never be placed downstream, as this could result in continuous pressure (12 hours of more) on the AVB. (i.e. spray nozzles, adapters, timer. ) If the device begins to leak it needs repaired or replaced.
Hose Bib Backflow protection

## Slide 14: Site Survey Process
Cross-Connection
Water Use Survey
Program Information

## Slide 15: AUTHORITY WAC 246-290-490
3(b) Element 1: The purveyor shall adopt a local ordinance, resolution, code, bylaw,
or other written legal instrument that:
(c) Element 2: The purveyor shall develop and implement procedures and schedules for
evaluating new and existing service connections to assess the degree of hazard posed
by the consumer’s premises to the purveyor’s distribution system and notifying the
consumer within a reasonable time frame of the hazard evaluation results. At a
minimum, the program shall meet the following:
(i) For connections made on or after April 9, 1999, procedures shall ensure that an initial
evaluation is conducted before water service is provided;
(i) Establishes the purveyor's legal authority to implement a cross ­connection control program;
(ii) Describes the operating policies and technical provisions of the purveyor’s cross-connection
control program; and
(iii) Describes the corrective actions used to ensure that consumers comply with the purveyor’s
cross­ connection control requirements.
(ii) For all other connections, procedures shall ensure that an initial evaluation is conducted in
accordance with a schedule acceptable to the department; and
(iii) For all service connections, once an initial evaluation has been conducted, procedures shall
ensure that periodic reevaluations are conducted in accordance with a schedule acceptable to
the department and whenever there is a change in the use of the premises.

## Slide 16: WORKING WITH THE AHJ WAC 246-290-490
(e) Under this section, purveyors are not responsible for eliminating or controlling cross­ connections
within the consumer's water system. Under chapter 19.27 RCW, the responsibility for cross
connection control within the consumer’s water system, i.e., within the property lines of the
consumer’s premises, lies with the authority having jurisdiction.
2(d) The purveyor shall coordinate with the authority having jurisdiction in all matters concerning cross­
connection control. The purveyor shall document and describe the coordination, including
delineation of responsibilities, in the written cross connection control program in the written cross
connection control program required in (e) of this subsection.
COK Authority
The authority for the City of Kirkland’s Cross Connection Control Program is derived from Chapter 603.0 of the Uniform Plumbing Code (UPC) including its Washington State Amendments as adopted by Kirkland Municipal Code 21.24.010. The UPC refers to WAC 246-290-490 and to the Washington State Department of Health regulations including the AWWA (American Water Works Association) Pacific Northwest Section’s of “Accepted Procedure and Practice in Cross Connection Control Manual.”
City of Kirkland Authority and Municipal Code:

## Slide 17: Getting Started
Obtain an active service connection list; (Meter information from finance).
Ensure you have a good tracking system of sites surveyed – Excel is a good tool if you do not have a software tracking program. You can keep annual data to see running totals.
  Include in your tracking:
    Acct#
    Device/Assembly#
    Business Name
    Business Owner
    Contact First and Last Name
    Physical Address
    Type of Assemblies Installed if any
    Hazard
    Is it Premise or In-Premise?
    Make, Model, SN, and Size of Assembly
    Date Surveyed
    Compliant – Yes or No
    Comments
    Follow up date
    Final Compliant – Yes or No
    # Of corrections
    Date Completed
Excel
Tracking

## Slide 18: PREPARATION IS THE KEY
(2)
(1)
Verify Site Location – look for the number of buildings and any other meters served on site.
  Map it out (GIS, Google)
Using you finance system or list provided to verify meter information – Manufacture, Size, Location, service addresses, owner information, tenant information especially for multi commercial sites.
  Can you find the meter?
  Get as much information you can
  and make notes on what you see.

## Slide 19: Notification of Water Use Survey
Notification of Water Use Survey
  The initial letter needs to explain what you are asking for and why and should include: EXAMPLE
    State Requirement– Found in PNWS AWWA, WAC 246-290-490 Element #4
    City Code Requirement and Responsibility
    How long this survey will take.
    Piping plans if available
    Who they should to contact for more details?
    Follow up date or Appointment Details – You should require a confirmation of appointment to ensure contact has been made.
  Keep a copy of the letter to take with you. (People like to claim they did not receive it and were not notified.)
    Example:
Acct# Business Name Type of Letter
4140-09500 CHAINLINE BREWING WATER USE SURVEY NOTIFICATION LETTER
4140-09500 CHAINLINE BREWING WATER USE SURVEY APPOINTMENT LETTER
4140-09500 CHAINLINE BREWING WATER USE SURVEY POST SURVEY LETTER OF COMPLIANCE
4140-09500 CHAINLINE BREWING WATER USE SURVEY POST SURVEY LETTER OF NON-COMPLIANCE
  Save it in a format you can easily track

## Slide 20: BE PREPARED: Tips For Being Ready
Confirming Appointment:
You may need to follow up if you have not received a confirmation of appointment.
  Explain what they should expect from this survey.
  It’s a great idea to get the full name and phone number of person you are meeting and set up your meeting location.
  Make sure you request a person who is familiar with the facility, plumbing system, and equipment processes.
  Take a copy of the appointment letter with you

## Slide 21: Preparing Your Water Use Survey Form
Prepare your survey form in advance.
There are many types of forms available. You can use one already provided by USC Manual Cross-Connection Control, IAPMO, electronic survey systems, or create your own.
COK Example – Commercial
IAPMO Example
USC Example
COK Survey Example-Residential

## Slide 22: Tools and Resources
Bring a flashlight, clipboard, forms, soap stone (for revealing SN on assemblies), small and long screwdriver for opening lids, gloves, face masks (medical facilities) and camera.
    NOTE: Photos should include assembly installation, assembly name plate (make model & SN), water using equipment including model information for equipment you are not familiar with. This will also you to research the item to see if additional protection is needed.
You should have reference materials with you. Examples include:
    List of Table 13
    List of Fixture isolations Hazards
      PNWS – AWWA Cross-Connection Control Manual
        Page 168 Chapter 5
    Janitors sink protection information - Mop Sink Best Practices
    Chemical Dispenser & AVB use information
    Installation standards (spec sheets)
Tools
Resources

## Slide 23: Performing Your Water Use Survey
You should always begin your survey at the meter. This will allow you to verify the meter serial number and installation of any backflows for premise including dedicated irrigation lines. You may find more than one meter. Document everything you see including the condition of the meter.
Rule #1 is to take your time. We are protecting public health. If the time is not convenient or you feel you are being rushed around, reschedule the appointment. It’s important to do a thorough survey!
It’s also best to allow the person you are walking with to determine the route of the survey for larger complexes. They have the most knowledge of how the property is set up. Before you begin your survey, go through your form and explain to them what you are looking for and you may be asking the same questions multiple times depending on how many buildings your visiting.
  Have one form per building or business so you can keep everything separate by meter and organized.

## Slide 24: Performing Water Use Survey Continued
What you need to know?
  How is the water being used?
  Do they have existing protection?
  What other water using equipment do they have that was not asked on the form?
  Verify – contact person, mailing address and follow up phone number.
You may need to get on a dirty floor, behind a hot oven, or under a sink to verify the make, model and serial number so be prepared.
It’s best to have two people during a survey but it okay if you do not. If you are the only one with the customer, talk them through the process as you tour the facility. Help educate them during the survey so if you find compliance issues, they will be able to understand what needs to be done before they receive the post survey letter.
Take pictures of everything and make sure you have your photos dated (public records request).
Finally, be sure to thank them for their time and give them a time frame on your follow up and post survey letter.
  Note: If you have a difficult customer, less may be better. Be ready, some folks don’t care and don’t want to be educated.

## Slide 25: POST SURVEY
Document your tracking log, database, and files
  Save site pictures with details (Device# Hazard SN., etc.) Link
Prepare compliance letter; Owner and tenant Link
  Include:
    Photos if possible (Make is simple)
    CC: all who need to know.
      Public Works Manager
      AHJ – Planning & Development
      Inspector
      Owner/Tenant
Set up a tracking system by date for easy access and follow up. Example: tickler file, calendar appointment etc.

## Slide 26: WHAT YOU MAY FIND
IMPROPER INSTALLATIONS

## Slide 27: Domestic Backflow – Improper Install (Unapproved Assembly): Before Correction

## Slide 28: Domestic Backflow – Proper Install (Approved Assembly): After Correction
The Double Check Valve Assembly (DCVA) is an approved backflow assembly consisting of two single check valves assembled within one body and furnished with four test cocks and two shut-off valves.

## Slide 29: Domestic Backflow – Improper Install (Unapproved Assembly): Before Correction

## Slide 30: Domestic Backflow – Proper Install: After Correction

## Slide 31: Domestic Water By-Pass without backflow protection
Unprotected By-Pass
Correction: Removed and capped

## Slide 32: Dock Water (Table 13) Severe High Health Hazard

## Slide 33: RPBA installed behind beverage dispenser hoses making testing & repair difficult.

## Slide 34: Support stand installed over assembly access – requiring removal for repair

## Slide 35: Installation over 5’ without permanent platform for testing and repairs

## Slide 36: SVB (Spill Resistant Vacuum Breaker) Installation – Over 5’
To test a SVB a tester is required to removed the Bonnet (Cap) and visually verify the water has drained and the air inlet fully opened.

## Slide 37: Application: Hood Scrubber Hazard: High Health Hazard Installation Issues:
UPC 603.4.9 Prohibited Location.
Backflow prevention devices with atmospheric vents or ports shall not be installed in pits, underground or in submerged locations. Backflow preventers shall not be located in any area containing fumes or aerosols that are toxic, poisonous, infectious, or corrosive.

## Slide 38: Chemical Container Resting & Leaking on assembly

## Slide 39: RPBA’s without 12” Relief Valve Clearance

## Slide 40: Chemical Dispensers
All Chemical Dispensers with a ASSE 1055B have internal air gaps and meet backflow prevention requirements.
The system will show an approval with ASSE 1055B label or engraving.
If the system does not show a label then protection is required with an RPBA or SVB.

## Slide 41: Janitor Closets with Chemical Dispensers
Protection Type:
SVB – Requires installation
12” Above Use
Protection Type: RPBA

## Slide 42
Irrigation Systems:
Improper Installations – Buried in dirt & mud with test port caps missing (cross-connection)

## Slide 43: QUESTIONS????
For more details on our Backflow Prevention Program,
please call us at 425-587-3913 or visit our new web page at: www.kirklandwa.gov/backflow-prevention